www.hf-radio.com.au ……Phone 07 3118 5265

How to change your (secret) telephone interconnect number on your Barrett 2050 with Ver 2.xx firmware fitted.

Detaching existing Default ID

- Hold “Menu” button down for 2 seconds to get into protected menu

- Scroll down to “Selcall Settings” using the up/down arrows (channel selector)

- Press “Enter”

- Scroll down to “Selcall OEM 2”---It will probably have the default No 99999 installed

- Press “Enter”

- Hold “Clear” Button down for 2 seconds

- You should then have a screen that says “Detach Self ID?”, Scroll down to “Yes” to detach  and press “Enter”…It should now show “Entry Detached” on the screen

Removing Existing ID

- Within the “Selcall Settings” menu goto “Self IDs”, press “Enter” and scroll to “Search Entries”

- Press “Enter”

- Use the scroll keys the select the Self ID you wish to erase.  This will normally be the previous default No “999999”

- Hold down the “Clear” key for at least 2 seconds – The erase entry verification screen should then appear.

Entering your New Self ID

- Within the “Selcall Settings” menu goto “Self IDs”, press “Enter” and scroll to “Add Entry”

- Press “Enter”

- Type in your new 6 digit Self ID

- Press “Enter”

- Input “Tel” for the address book name via the keypad

- Press “Enter”

- Scroll to “OEM”(Not International) in the “Type” field

- Press “Enter

- It should then display “New Entry”

- Press “Clear” button a few times to go back to standard channel display

Setting the new self ID as default

- Hold “Menu” button down for 2 seconds to get into protected menu

- Scroll down to “Selcall Settings” using the up/down arrows (channel selector)

- Press “Enter”

- Scroll down to “Selcall OEM 2”---It should say “N/A” written on the screen

- Press “Enter”

- Scroll to your new 6 digit self ID

- Press “Enter”

- It should say “Selcall OEM 2 Selected”

- Your new 6 digit self ID should now be set up as your default for phone calls Via HF-Tel

- Press clear a few times to go back to the standard channel display

Checking your Default self IDS

- While in the normal channel display, quickly press “Menu”

- You should see “Identification” on the screen

- Press “Enter”

- Press the “3” button twice and you should then see “Selcall IDs – You should see your standard 4 digit self ID in “OEM1”, and your secret telephone self ID “OEM2” positions

- Press Clear a couple of times to go back to the standard channel display

If all is OK, then your HF-TEL service should now be ready to use